## Slide 1: Totalys-system Workflow at Ahus, Norway
Anna Wittersø

## Slide 2: Regional laboratory for Cervix-screening
2,6 million people
11 state hospitals
HPV primary screening age 34-69
From 10 to 3 regional laboratories in the national screeningprogram
  Akershus University Hospital
    Expect around 70 000 cervical samples in 2022
      HPV only: 56 %
      Cytology only 26 %
      HPV and cytology 18 %

## Slide 3: Registration
Requests:
  Electronic
  Paper
Integrated in the LIMS: Check patienthistory for correct workline.
HPV, Cytology or both according to national guidelines.
  If co-test HPV and cytology – Cytology first
  HPV primary-screening, if positive  Cytology
Normal day average:
  140 HPV (primary HPV)
  130 Cytology (co test and primary cytology)

## Slide 4: Linking C-tube – SurePath-vial
Extra label for C-tubes printed during registration.
  Sample-ID, Patient-ID, QR-code and workitem (decides HPV, Cytology or both)
C-tubes labeled when loading the tray
Link the Sample-ID to the C-tube-ID by scanning both QR-codes on remote station.

## Slide 5: MultiProscessor
Printing of slides programmed in datalink
  When proscessing the samples in MultiProscessor the slide print is activated.
  You always have the right slides for the batch
  Possible to reprint if problem with the printer during printing (bad print etc).

## Slide 6: SlidePrep -
Slideprep
  2 instruments if many samples
After rinsing - xylen
Coverslipping – Leica Spectra

## Slide 7: Check each slide – rerun?
All slides are checked macorscopic
  If it looks scant - we check in microscop and order rerun with 800 µl if few sqamous cells. Both slides are screened.
  Picture:
    left slide – rerun
    right slide ok
  Airbubbles? Remove coverslip and cover again (manually)

## Slide 8: Scanning in FocalPoint
All slides, but slides that need rerun or Cito-samples are going directly to screening.
Scanning overnight

## Slide 9: Screening
Guided screening - focalpoint
  Not all samples
  Ergonomic challenge for some screeners
  Many slides have HPV testing and need rescreening
Screeninghistory – access to history in national cancer-register
Symptoms, clinical information and HPV-status
Rescreening
  Symptoms
  HPV positive
  Other reasons

## Slide 10: Digital imaging
Regional prosess for regional solution
  Histology first
Need scanning in different focus for cytology
No plans for digital imaging on cytology the next years

## Slide 11: Improvements?
Multiprocessor
Check for syringes before processing
Sensor for measuring density reagent and trisbuffer remaining

## Slide 12: Thank you!